## Slide 1: Module 1. MicroPython Basic
MicroPython + NodeMCU-ESP32S
safyzan salim
019 622 0575
IoT with ESP32 Training|Rev01-SEPT2023|

## Slide 2
Theoretically:
√ To run Python code on an ESP32 microcontroller, you need to flash ESP32’s MicroPython firmware.
√ MicroPyton ports Python 3.x, designed to run on microcontrollers, small embedded systems and is tailored for resource-constrained environments like the ESP32.
√ Link to download ESP32’s MicroPython firmware:
https://micropython.org/download/ESP32_GENERIC/
√ Python IDE: Thonny IDE
https://thonny.org/
Rev01 Sept2023
MicroPython + NodeMCU-ESP32S

## Slide 3
Rev01 Sept2023
>> Do refer at this link for further details: https://micropython.org/download/
Listed are Arduino families that can be used for MicroPython:
MicroPython + NodeMCU-ESP32S

## Slide 4
Rev01 Sept2023
1. Downloading MicroPython Firmware.
Download from https://micropython.org/download
Select the appropriate board.
MicroPython + NodeMCU-ESP32S

## Slide 5
1. Downloading MicroPython Firmware.
Rev01 Sept2023
Choose any dot bin version releases firmware.
Nightly builds are unstable with fresh features and bugs not thoroughly tested.
Normally, select one or two version lower from the recent version.
MicroPython + NodeMCU-ESP32S
e.g.: v1.19.1(2022-06-18).bin

## Slide 6
2. Thonny Python IDE: Download & Install
Rev01 Sept2023
Download from https://thonny.org/
Thonny is a beginner friendly Python IDE.
To erase & flush new firmware to ESP32S with the help of ESP tool.
Act as Python editor.
MicroPython + NodeMCU-ESP32S

## Slide 7
Rev01 Sept2023
2. Thonny Python IDE: Run Thonny
MicroPython + NodeMCU-ESP32S

## Slide 8
Rev01 Sept2023
Install plug-ins first.
Tools > Manage plug-ins.
Connect the ESP32S to your system.
2. Thonny Python IDE: Flushing New ESP32 Firmware.
MicroPython + NodeMCU-ESP32S

## Slide 9
Rev01 Sept2023
Type esptool & click Search on PyPi button.
Click esptool to install.
2. Thonny Python IDE: Flushing New ESP32 Firmware.
MicroPython + NodeMCU-ESP32S

## Slide 10
Rev01 Sept2023
esptool installed.
2. Thonny Python IDE: Flushing New ESP32 Firmware.
MicroPython + NodeMCU-ESP32S

## Slide 11
Rev01 Sept2023
To install Firmware.
Tools > Options
2. Thonny Python IDE: Flushing New ESP32 Firmware.
MicroPython + NodeMCU-ESP32S

## Slide 12
Rev01 Sept2023
Go to Interpreter tab.
Select MicroPython (ESP32).
2. Thonny Python IDE: Flushing New ESP32 Firmware.
MicroPython + NodeMCU-ESP32S

## Slide 13
Rev01 Sept2023
Port: Choose the appropriate comm port of your ESP32S.
If port not detected, check your ESP32S connection to your laptop/PC.
2. Thonny Python IDE: Flushing New ESP32S Firmware.
MicroPython + NodeMCU-ESP32S

## Slide 14
Rev01 Sept2023
Click Install or Update Micropython link.
2. Thonny Python IDE: Flushing New ESP32 Firmware.
MicroPython + NodeMCU-ESP32S

## Slide 15
Rev01 Sept2023
Target Port: Which port the EPS32S is connected.
: browse the downloaded dot bin file from micropython.org.
Ensure that the Erase flash before installing is checked.
2. Thonny Python IDE: Flushing New ESP32S Firmware.
MicroPython + NodeMCU-ESP32S

## Slide 16
Rev01 Sept2023
Proceed with clicking Install button.
2. Thonny Python IDE: Flushing New ESP32S Firmware.
MicroPython + NodeMCU-ESP32S

## Slide 17
Rev01 Sept2023
Click Done! to view detail installation.
Click Close button to go to previous page.
2. Thonny Python IDE: Flushing New ESP32S Firmware.
MicroPython + NodeMCU-ESP32S

## Slide 18
Rev01 Sept2023
Click OK button upon complete installation.
2. Thonny Python IDE: Flushing New ESP32S Firmware.
MicroPython + NodeMCU-ESP32S

## Slide 19
Rev01 Sept2023
2. Thonny Python IDE: Flushing New ESP32S Firmware.
MicroPython + NodeMCU-ESP32S
Scripts that type at Shell, will respond immediately at ESP32.
To stop click Stop button at the top.
Click Run button to resume operation.

## Slide 20
Rev01 Sept2023
import machine
led = machine.Pin(2, machine.Pin.OUT)
led.on()
led.off()
led.value(1)
led.value(0)
led.value(true)
led.value(false)
2. Thonny Python IDE: Point to Shell tab
Type the Python script line by line & press enter.
Please refer to ESP32S & observe the output .
MicroPython + NodeMCU-ESP32S

## Slide 21
Rev01 Sept2023
import machine
led = machine.Pin(2, machine.Pin.OUT)
import time
while True:
led.on()
time.sleep(0.5)
led.off()
time.sleep(0.5)
New
Open
Run Current Script
Stop / Restart
MicroPython + NodeMCU-ESP32S
2. Thonny Python IDE: Point to Shell Tab or A Tab
Type at A if you wish to save the file
A

## Slide 22
Rev01 Sept2023
MicroPython + NodeMCU-ESP32S
2. Thonny Python IDE: Saving Your Works
You have two options to save your file: This computer or MicroPython device.
Name you file as main.py if you wish to save into MicroPython board & any name if you wish to save into your drive.

## Slide 23
Rev01 Sept2023
MicroPython + NodeMCU-ESP32S
2. Thonny Python IDE: Saving Your Works
Your microcontroller
Your laptop / PC

## Slide 24
Rev01 Sept2023
MicroPython + NodeMCU-ESP32S
Remember:
1. Always ensure that the you have selected the right Comm Port to communicate with ESP32.
Tools>Option>Interpreter Tab
2. Only upload MicroPython firmware once, unless you have uploaded Arduino ESP32 firmware, then you have to click the Install or update MicroPython link.
3. Open Arduino IDE, select ESP32 board, its port & upload Arduino sketch as usual.

## Slide 25
Rev01 Sept2023
MicroPython + NodeMCU-ESP32S
END